Unit 4: Solution Chemistry

Content Outline: Solubility (4.7)

I.       Solubility

A.   Solubility is the ability of one substance to dissolve in another at a given temperature and pressure.

- Solubility is expressed in terms of the amount of solute that will dissolve in a given amount of solvent to produce a saturated solution.  The maximum grams of solute that will dissolve in 100gram of solvent at a given temperature

II.        Solution equilibrium is reached when the physical state in which the opposing process of dissolution and

crystallization of a solute occurs at equal rates.

- Insolubility is the inability of one substance to dissolve in another substance. (For example, oil will not dissolve in water, such as salad dressing.)

IV.       Saturated vs Unsaturated Solutions:

- Saturated Solutions - A solution that contains the maximum amount of dissolved solute is described as a saturated solution.

- Unsaturated Solutions - A solution that contains less solute than a saturated solution under the existing conditions is an unsaturated solution.

- Supersaturated Solutions - A supersaturated solution is a solution that contains more dissolved solute than a saturated solution under the same conditions.

- Factors Involving Solubility

- Stirring, increasing surface area (small particle size) and increasing temperature will all increase the rate at which a solid solute is dissolved in a solvent.

- Gases increase in solubility if there is high pressure or low temperature.  Stirring or shaking does not increase the rate of solubility in gases.

- Henry’s Law:  one of the gas laws formulated by William Henry in 1803 and states: "At a constant temperature, the amount of a given gas that dissolves in a given type and volume of liquid is directly proportional to the partial pressure of that gas in equilibrium with that liquid." An equivalent way of stating the law is that the solubility of a gas in a liquid is directly proportional to the partial pressure of the gas above the liquid.  If the pressure above the liquid is less, then the gas in the liquid will escape the solution.

- Liquids that dissolve in another liquid are miscible.  Liquids that do not dissolve in another liquid are immiscible.

VI.  Solubility Table and Curves

- Solubility curves are a graphical representation and can be used to determine if a particular solution is soluble at a given temperature.

See the example below:

- A solubility table is a reference used to determine if a solute is soluble in 100grams of water.  Usually, exceptions or slight variations are also listed.  See the example below from ChemTeam.